## Slide 1: ﻿Master’s Thesis 2023
Advanced control implementations with Modelica
Carl Magnus Bøe MSc Industrial IT and Automation
﻿Faculty of Technology, Natural Sciences and Maritime Sciences
GitHub: https://github.com/cmbNor/Advanced-Control-Implementation-with-Modelica
Campus Porsgrunn
1. Introduction
In the absence of inherent support for advanced control methods in Modelica, the current workflow as displayed in Figure 1, consisting of generating models within Modelica. Subsequently, the models are exported as functional mock-up units (FMUs) to SIMULINK. Within SIMULINK the MPC block in the model predictive control toolbox is utilized to compute the control signal.
3. Model of Air Heater
Three models of the air heater were implemented in OpenModelica. These models are based on first-principles, transfer function, and discrete and continuous-time state space models, as illustrated in the OpenModelica implementation shown in Figure 3.
5. Results of Air Heater FMU and MPC in Python
In a Python script, model predictive control (MPC) simulations were conducted for both a first-principles model and a FMU of the air heater. Figure 5 illustrates the resulting plot generated from these simulations.
2. Problem Description and Objective
Yara's goal is to enhance efficiency by centralizing the entire system within Modelica. An option under consideration involves the integration of an MPC block directly into the Modelica environment with the use of external objects as displayed in Figure 2.
4. Calling External C code in Modelica
The Modelica external object class served a crucial function in overseeing memory allocation for storing computational variable values. It enabled the execution of a function call to an external C function responsible for carrying out optimization processes. The results of this optimization were then communicated back to the Modelica environment. The optimization procedure itself made use of the NLopt library for C, with the cost function delineated in Figure 4 serving as its foundation.
6. Conclusion
﻿The thesis provides insights into advanced control implementation strategies within the Modelica framework and serves as a practical user manual. The comprehensive explanations provided are intended to assist in the implementation of these control strategies together with the associated GitHub repository.
Figure 1: Current workflow
Figure 2: Future workflow
Figure 3: Implemented models in OpenModelica
Figure 4: Optimization
Figure 5: MPC simulation results