## Slide 1: Advanced Control Implementations with Modelica
FMH606 Master’s Thesis 2023 Industrial IT and Automation Carl Magnus Bøe Supervisor USN: Finn Haugen Supervisor Yara: Anushka Perera Repository: https://github.com/cmbNor/Advanced-Control-Implementation-with-Modelica

## Slide 2: Introduction
Background information
Modelica
Functional Mock-up Interface (FMI)
SIMULINK
Model Predictive Control Toolbox
Open-source equation-based modelling language
Graphical and text based
Multi domain support
Standard library
  1600 components
  1350 distinct function
Vendor neutral standard for model exchange
Defines a container and an interface
Open standard
Commercial tool from MathWorks
Graphical extension of MATLAB
Used to simulate and analyze dynamic models
Block based
Commercial toolbox for SIMULINK
Example code
SIMULINK blocks
Notes: Model Exchange-needs external solver
Simple and fast
Co-simulation- includes solver
Flexible and slower

## Slide 3: Introduction
Background information
Modelica
External Object
Modelica
Modelica
Functional Mock-up Interface (FMI)
SIMULINK
Model Predictive Control Toolbox
Notes: Initial scope of thesis

## Slide 4: Introduction
Revised scope
Modelica
External Object
Modelica
External Object
FMU
Python

## Slide 5: Existing Options
Linear MPC Modelica Library
  Open-source
  Last updated 2016
  Not compatible with Modelica 4.0
JModelica
  Discontinued in 2019
  Assimulo
  PyFMI
  FMI Library
FMPy - Dassault Systèmes
  Free Python FMI library
  Graphical user interface
    Validate FMUs
    Export to Jupyter Notebook, Modelica and Cmake
    Web App
NLopt
  Open-source optimization library
  C, C++, MATLAB, Fortran, Python among others
  Collection of several algorithms from different contributors
Notes:   Linear MPC Modelica Library
    State space model
    The demo models work when converted to Modelica 4.0 but not able to add air heater model
  Jmodelica
    Assimulo
      Python simulation packages - Solver
    PyFMI
      Python package to load and simulate FMUs
    FMI Library
      C package to load and simulate FMUs
  FMPy - Dassault Systèmes (desså system)
  NLopt

## Slide 6: Air Heater Model
First-principles, transfer function, and state space models
First-principles:
Transfer Function:
State Space:
Notes: 3.5 models implemented
Air heater model - Time constant with time delay process dynamics
  Time constant
  Rate of change in temperature
  Heater gain
  Time delay
FIRST-PRINCIPLE
  Implemented as a model in Modelica based on first-principles / mechanistic model
  Equation based – Heater gain, Time constant and timedelay
TRANSFERFUNCTION
  Basic Modelica blocks
    Time delay
    Transfer function
STATE SPACE
  Implemented with the use Python Control Systems Library
  Build transfer function, then use series function to merge transfer and timedelay (padé)
All models simulated in same model, with same changes in setpoint

## Slide 7: Air Heater Model
Simulation of first-principle, transfer function, and state space models
Notes: Control signal sequence

## Slide 8: Air Heater Model
Simulation results for first-principle, transfer function, and state space models
Notes: Order of padé approximation = 10

## Slide 9: Air Heater Model
Simulation results for first-principle, transfer function, and state space models
Notes: Order of padé approximation = 10
Not a step change

## Slide 10: Calling External C Code in Modelica
Overview
Basic functions with one return variable
Needs a Modelica block or model as a wrapper
Modelica Function
Modelica External Object
Extended functionality and complexity
Enables reading and writing of variables from external memory across C and Modelica

## Slide 11: Calling External C Code in Modelica
Implementation with the use of Modelica function

## Slide 12: Calling External C Code in Modelica
Implementation with the use of external objects
Notes: Error: C Destructor writes object destroyed to the screen

## Slide 13: Calling External C Code in Modelica
Results

## Slide 14: NLopt
Overview
NLopt
Version
Examples of solving a multivariate optimization problem in OpenModelica by calling a NLopt function in C
Examples of solving a univariate optimization problem in OpenModelica by calling a NLopt function in C
Basic example for calling external C functions in NLopt from OpenModelica and returning values to OpenModelica
Notes: HALVEIS – Sjekk tiden 20min

## Slide 15: NLopt
Multivariate optimization

## Slide 16: FMU of Air Heater in Python
Overview

## Slide 17: FMU of Air Heater in Python
Results

## Slide 18: FMU of Air Heater in Python
Results
Notes: Correlation map

## Slide 19: FMU of Air Heater with MPC in Python
Overview
Based on Python MPC source code from TechTeach.no
  Nonlinear model
FMU implemented the same way as the PI example
FMU runs in parallel with nonlinear model of the air heater
General
Set the FMU simulation parameters
Connect model value references to variables
  Enables get/set in simulation
Import the air heater FMU object
Set initial values for the set values
Simulate system with doStep()
Get and set variables for each timestep in simulation
Python - FMPy

## Slide 20: FMU of Air Heater with MPC in Python
Results

## Slide 21: FMU of Air Heater with MPC in Python
Results

## Slide 22: FMU of Air Heater with MPC in Python
Measures

## Slide 23: Conclusion
Both methods of implementation have their strengths and weaknesses
External objects in Modelica
    Fast calculations
    Complex
FMU in Python
    Versatile
    Widespread online support

## Slide 24: Future Work
Develop an external object designed to utilize FMUs in the optimization
  Removes the requirement for transferring the equation from Modelica to C
  Can perform optimization independent of model type
Variables and parameters to be handled in the Modelica environment
Modelica
FMU
C function
Export FMU
Import FMU
Optimization parameters
Return results
Notes: Model type Linear or nonlinear models.

## Slide 25
Thank you for the attention

## Slide 26
DRAFTS

## Slide 27
Modelica
FMU
C function
Export FMU
Import FMU
Optimization parameters
Return results

## Slide 28: Introduction
Modelica
Equation-Based Modeling:
  Uses equations for dynamic system representation
Open Standard:
  Collaboration among different simulation tools, libraries, and Modelica-compliant environments
Multi-Domain Support:
  Model complex systems across diverse domains
Graphical and Text-Based Options:
  Offers flexibility with both graphical and text-based modeling
Functional Mock-up Unit (FMU) for Interconnectivity:
  Supports Functional Mock-up Units for model exchange and co-simulation
Notes: Equation-Based Modeling:
Modelica uses equations to describe system behavior, allowing for a natural representation of dynamic systems.
Multi-Domain Support:
It's designed to model complex systems across diverse engineering domains like electrical, mechanical, thermal, and fluid systems.
Functional Mock-up Units (FMUs):
ModelExchange-needs external solver – Simple and fast ; Co-simulation-FMU includes solver – Flexible and slower
Vendor neutral
Declarative Modeling:
The language takes a declarative approach, focusing on defining relationships between variables rather than specifying solution algorithms(procedual).
Graphical and Textual Options:
MODELICA STANDARD LIBRARY
1600 components and 1350 distinct function

## Slide 29: Existing Options
JModelica
  Discontinued in 2019
  Three packages moved to GitHub:
  Assimulo
    Python simulation packages
  PyFMI
      Load and simulate FMUs
  FMI Library
    C package to load and simulate FMUs

## Slide 30: Existing Options
FMPy - Dassault Systèmes
  Free Python library
  Graphical user interface
    Validate FMUs
    Export to Jupyter Notebook, Modelica and Cmake
    Read model data
  Web App to share FMUs with anyone in a browser

## Slide 31: Existing Options
NLopt
  Open-source library
    C, C++, MATLAB, Fortran, Python among others
  Collection of several algorithms from different contributors
Set up the Optimizer Object
Define optimizer algorithm and number of optimization variables
Set up Objective Function
Combine the optimizer object and the function to be optimized
Set Bounds
Set upper, lower, equality and inequality bounds based on algorithm capability
Optimize the Problem!
Use the optimizer together with the defined minimum cost and the optimization variable

## Slide 32: Air Heater Model
First-principles model in Modelica
Notes: Air heater model - Time constant with time delay process dynamics
Implemented as a model in Modelica

## Slide 33: Air Heater Model
Transfer function

## Slide 34: Air Heater Model
State space models

## Slide 35: Air Heater Model
Model evaluation

## Slide 36: FMU of Air Heater with PI-controller in Python
Overview
Set the FMU simulation parameters
Connect model value references to variables
  Enables get/set in simulation
Import the air heater FMU object
Set initial values for the set values
Simulate system with doStep()
Get and set variables for each timestep in simulation
Python - FMPy
OpenModelica

## Slide 37: FMU of Air Heater with PI-controller in Python
Results

## Slide 38: FMU of Air Heater with PI-controller in Python
Measures